DS232A Dual RS-232 Transmitter/Receiver

FEATURES

ƒ	Compatible with LT1181A and MAX232A

ƒ	High data rate - 250 kbits/sec under load

ƒ	16-pin DIP or SOIC package

ƒ	20-pin TSSOP package for height restricted

applications

ƒ	Operate from single +5V power

ƒ	Meets all EIA-232E and V.28 specifications

ƒ	Uses small capacitors: 0.1 μF

	Optional industrial temperature range

available (-40°C to +85°C)

ORDERING INFORMATION

DS232A	16-pin DIP

DS232A-N	16-pin DIP (Industrial) DS232AR	16-pin SOIC (150-Mil)

DS232AR-N   16-pin SOIC (150-Mil) (Industrial) DS232AS	16-pin SOIC (300-Mil)

DS232AS-N	16-pin SOIC (300-Mil) (Industrial) DS232AE	20-pin TSSOP

DS232AE-N	20-pin TSSOP (Industrial)

DESCRIPTION

PIN ASSIGNMENT

| C1+ | 1 | 16 | VCC |
| --- | --- | --- | --- |
| V+ | 2 | 15 | GND |
| C1- | 3 | 14 | T1OUT |
| C2+ | 4 | 13 | R1IN |
| C2- | 5 | 12 | R1OUT |
| V- | 6 | 11 | T1IN |
| T2OUT | 7 | 10 | T2IN |
| R2IN | 8 | 9 | R2OUT |

16-Pin DIP AND SOIC

T

20-Pin TSSOP

PIN DESCRIPTION

VCC	- +5-Volt Supply

GND	- Ground

V+	 - Positive Supply Output V-	 - Negative Supply Output T1IN, T2IN	- RS-232 Driver Inputs T1OUT, T2OUT	 - RS-232 Driver Outputs R1IN, R2IN	- Receiver Inputs

R1OUT, R2OUT	- Receiver Outputs

C1+, C1-	- Capacitor 1 Connections

C2+, C2-	- Capacitor 2 Connections

The DS232A is a dual RS-232 driver/receiver pair that generates RS-232 voltage levels from a single +5- volt power supply. Additional ±12-volt supplies are not needed since the DS232A uses on-board charge pumps to convert the +5-volt supply to ±10 volts. The DS232A is fully compliant with EIA RS-232E and V.28/V.24 standards. The DS232A contains two drivers and two receivers. Driver slew rates and data rates are guaranteed up to 250k bits/sec. The DS232A operates with only 0.1 μF charge pump capacitors.

OPERATION

The diagram in Figure 1 shows the main elements of the DS232A. The following paragraphs describe the function of each pin.

1 of 10	112099

FUNCTIONAL DIAGRAM OF DS232A Figure 1

NOTE: C5 is a recommended decoupling capacitor which is the same value as C1, C2, C3, and C4. ( ) Are for TSSOP package only.

PIN DESCRIPTIONS

VCC, GND: DC power is provided to the device on these pins. VCC is the +5-volt input.

V+: Positive supply output (RS-232). V+ requires an external storage charge capacitor of at least 0.1 μF. A larger capacitor (up to 10 μF) can be used to reduce supply ripple.

V-: Negative supply output (RS-232). V- requires an external storage capacitor of at least 0.1 μF. A

larger capacitor (up to 10 μF) can be used to reduce supply ripple.

T1IN, T2 IN: Standard TTL/CMOS inputs for the RS-232 drivers. The inputs of unused drivers can be left unconnected since each input has a 400 kΩ pullup resistor.

T1OUT, T2 OUT: Driver outputs at RS-232 levels. Driver output swing meets RS-232 levels for loads up to

3 kΩ. These driver outputs provide current necessary to meet RS-232 levels for loads up to 2500 pF.

R1 IN, R2 IN: Receiver inputs. These inputs accept RS-232 level signals (±25 volts) into a protected 5 kΩ

terminating resistor. Each receiver provides 0.5V hysteresis (typical) for noise immunity.

R1 OUT, R2 OUT: Receiver outputs at TTL/CMOS levels.

C1+, C1-, C2+, C2-: Charge pump capacitor inputs. These pins require two external capacitors (0.1 μF minimum, 10 μF maximum and should be the same size as C3 and C4). Capacitor 1 is connected between C1+ and C1-. Capacitor 2 is connected between C2+ and C2-. Capacitor C1 can be omitted if +12 volts is connected directly to V+. Likewise, C2 can be omitted if -12V is connected directly to V-.

DUAL CHARGE PUMP CONVERTERS

The DS232A has a two-stage on-board charge pump circuit that is used to generate ±10 volts from a single +5-volt supply. In the first stage, capacitor C1 doubles the +5V supply to +10 volts which is then stored on capacitor C3. The second stage uses capacitor C2 to invert the +10V potential to -10V. This charge is then stored on capacitor C4. The ±10-volt supplies allow the DS232A to provide the necessary output levels for RS-232 communication. The DS232A will operate with charge pump capacitors as low as 0.1 μF. Larger capacitors (up to 10 μF) can be used to reduce supply ripple.

RS-232 DRIVERS

The two RS-232 drivers are powered by the internal ±10-volt supplies generated by the on-board charge pump. The driver inputs are both TTL and CMOS compatible.  Each input has an internal 400 kΩ pullup resistor so that unused transmitter inputs can be left unconnected.  The open circuit output voltage swing is from (V+ - 0.6) to V- volts. Worst case conditions for EIA-232E/V.28 of ±5-volt driving a 3 kΩ load and 2500 pF are met at maximum operating temperature and VCC  equal to 4.5 volts. Typical voltage swings of ±8 volts occur when loaded with a nominal 5 kΩ RS-232 receiver. As required by EIA-232E and V.28 specifications, the slew rate at the output is limited to less than 30 volts/μs. Typical slew rates are 20 volts/μs unloaded and 12 volts/μs with 3 kΩ and 2500 pF load. These slew rates allow for bit rates of over 250k bits/s. Driver outputs maintain high impedance when power is off.

RS-232 RECEIVERS

The two receivers conform fully to the RS-232E specifications.	The input impedance is typically 5

kΩ and can withstand up to ±25 volts with or without VCC applied.  The input switching thresholds are within the ±3-volt limit of RS-232E specification with an input threshold low of 0.8 volts and an input threshold high of 2.4 volts. The receivers have 0.5 volts of hysteresis (typical) to improve noise rejection. The TTL/CMOS compatible outputs of the receivers will be low whenever the RS-232 input is greater than 2.4 volts. The receiver output will be high when the input is floating or driven between +0.8 volts and -25 volts.

ABSOLUTE MAXIMUM RATINGS*

Absolute Maximum Ratings

VCC	-0.3V to +7.0V

V+	(VCC-0.3V) to +14V

V-	+0.3V to -14V

Input Voltages

TIN	-0.3V to (VCC+0.3V) RIN	±30V

Output Voltages

TOUT	(V+ + 0.3V) to (V- - 0.3V) ROUT	-0.3V to (VCC+ 0.3V)

Short Circuit Duration, TOUT	Continuous

*	This is a stress rating only and functional operation of the device at these or any other conditions above those indicated in the operation sections of this specification is not implied. Exposure to absolute maximum rating conditions for extended periods of time may affect reliability.

RECOMMENDED DC OPERATING CONDITIONS	(0°C to 70°C)

| PARAMETER | SYMBOL | MIN | TYP | MAX | UNITS | NOTES |
| --- | --- | --- | --- | --- | --- | --- |
| Operating Supply Voltage | VCC | 4.5 |  | 5.5 | V | 1 |

DC ELECTRICAL CHARACTERISTICS	(0°C to 70°C)

| PARAMETER | SYMBOL | MIN | TYP | MAX | UNITS | NOTES |
| --- | --- | --- | --- | --- | --- | --- |
| Power Supply Current (No Load) | ICC1 |  | 4 | 10 | mA |  |
| Power Supply Current (3 kΩ Load All Outputs) | ICC2 |  | 15 |  | mA |  |
| RS-232 Transmitters |  |  |  |  |  |  |
| Output Voltage Swing | VORS | ±5 | ±8 |  | V | 2 |
| Input Logic Threshold Low | VTTL | 0.8 | 1.4 |  | V |  |
| Input Logic Threshold High | VTTH |  | 1.4 | 2.0 | V |  |
| Maximum Data Rate | fD | 250 | 350 |  | k bits/s |  |
| Logic Pullup/Input Current | IPU |  | 5 | 40 | μA |  |
| Transmitter Output Resistance | ROUT | 300 | 10M |  | Ω | 3 |
| Output Short-Circuit Current | ITSC | ±15 | ±30 | ±100 | mA | 4 |

DC ELECTRICAL CHARACTERISTICS (continued)	(0°C to 70°C)

| RS-232 Receivers |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| RS-232 Input Voltage Operating Range | VIR | ±25 | ±30 |  | V |  |
| RS-232 Input Threshold Low | VRTL | 0.8 | 1.3 |  | V |  |
| RS-232 Input Threshold High | VRTH |  | 1.8 | 2.4 | V |  |
| RS-232 Input Hysteresis | VHY | 0.2 | 0.5 | 1 | V |  |
| RS-232 Input Resistance | RIN | 3 | 5 | 7 | kΩ |  |
| TTL/CMOS Output Voltage Low | VROL |  | 0.2 | 0.4 | V | 5 |
| TTL/CMOS Output Voltage High | VROH | 3.5 | VCC-0.2 |  | V | 6 |
| TTL/CMOS Output Short Circuit Current (VOUT=GND) | IRSC | -2 | -10 |  | mA |  |
| TTL/CMOS Output Short Circuit Current (VOUT=VCC) | IRSC | 10 | 30 |  | mA |  |

AC ELECTRICAL CHARACTERISTICS	(0°C to 70°C)

| PARAMETER | SYMBOL | MIN | TYP | MAX | UNITS | NOTES |
| --- | --- | --- | --- | --- | --- | --- |
| Transition Slew Rate | tSR | 6 | 12 | 30 | V/μs | 7 |
| Transmitter Propagation Delay TTL to RS-232 | tPHLT tPLHT |  | 1.3 1.5 | 3.5 3.5 | μs μs |  |
| Receiver Propagation Delay RS-232 to TTL | tPHLR tPLHR |  | 0.5 0.6 | 1 1 | μs μs |  |
| Transmitter + to - Propagation Delay Difference | tPHLT -tPLHT |  | 300 |  | ns |  |
| Receiver + to - Propagation Delay Difference | tPHLR -tPLHR |  | 100 |  | ns |  |

NOTES:

1.   All voltages are referenced to ground.

2.   All transmitter outputs loaded with 3 kΩ to ground

3.   VCC = V+ = V- = 0V; VOUT = ±2V.

4.   VOUT = 0V.

5.   IOUT = 3.2 mA.

6.   IOUT = -1.0 mA.

7.   CL = 50 pF - 2500 pF; RL = 3 kΩ - 7 kΩ; VCC = 5V; TA = 25°C.

TRANSMITTER PROPAGAION DELAY TIMING Figure 2

RECEIVER PROPAGATION DELAY TIMING Figure 3

16-PIN DIP (300-MIL)

| PKG | 16-PIN |
| --- | --- |
| DIM | MIN | MAX |
| A IN. MM | 0.740 18.80 | 0.780 19.81 |
| B IN. MM | 0.240 6.10 | 0.260 6.60 |
| C IN. MM | 0.120 3.05 | 0.140 3.56 |
| D IN. MM | 0.300 7.62 | 0.325 8.26 |
| E IN. MM | 0.015 0.38 | 0.040 1.02 |
| F IN. MM | 0.120 3.04 | 0.140 3.56 |
| G IN. MM | 0.090 2.29 | 0.110 2.79 |
| H IN. MM | 0.320 8.13 | 0.370 9.40 |
| J IN. MM | 0.008 0.20 | 0.012 0.30 |
| K IN. MM | 0.015 0.38 | 0.021 0.53 |

16-PIN SOIC (150-MIL)

16-PIN SOIC (300-MIL)

20-PIN TSSOP

# Text boxes

| C1+ | 1 | 20 | NC |
| --- | --- | --- | --- |
| V+ | 2 | 19 | VCC |
| C1- | 3 | 18 | GND |
| C2+ | 4 | 17 | T1OUT |
| NC | 5 | 16 | R1IN |
| C2- | 6 | 15 | R1OUT |
| V- | 7 | 14 | NC |
| NC | 8 | 13 | T1IN |
| 2OUT | 9 | 12 | T2IN |
| R2IN | 10 | 11 | R2OUT |

| PKG | 16-PIN |
| --- | --- |
| DIM | MIN | MAX |
| A IN. MM | 0.053 1.35 | 0.069 1.75 |
| A1 IN. MM | 0.004 0.10 | 0.010 0.25 |
| A2 IN. MM | 0.048 1.24 | 0.062 1.57 |
| B IN. MM | 0.012 0.30 | 0.020 0.50 |
| C IN. MM | 0.007 0.17 | 0.011 0.28 |
| D IN. MM | 0.386 9.80 | 0.393 9.98 |
| E IN. MM | 0.050 BSC 1.27 BSC |
| E1 IN. MM | 0.150 3.81 | 0.158 4.01 |
| H IN. MM | 0.230 5.84 | 0.244 6.20 |
| L IN. MM | 0.016 0.40 | 0.050 0.89 |
| Θ | 0° | 8° |

| PKG | 16-PIN |
| --- | --- |
| DIM | MIN | MAX |
| A IN. MM | 0.094 2.39 | 0.105 2.67 |
| A1 IN. MM | 0.004 0.102 | 0.012 0.30 |
| A2 IN. MM | 0.089 2.26 | 0.095 2.41 |
| b IN. MM | 0.013 0.33 | 0.020 0.51 |
| C IN. MM | 0.009 0.229 | 0.013 0.33 |
| D IN. MM | 0.398 10.11 | 0.412 10.46 |
| E IN. MM | 0.050 BSC 1.27 BSC |
| E1 IN. MM | 0.290 7.37 | 0.300 7.62 |
| H IN. MM | 0.398 10.11 | 0.416 10.57 |
| L IN. MM | 0.016 0.40 | 0.040 1.02 |
| Θ | 0° | 8° |

| DIM | MIN | MAX |
| --- | --- | --- |
| A MM | - | 1.10 |
| A1 MM | 0.05 | - |
| A2 MM | 0.75 | 1.05 |
| C MM | 0.09 | 0.18 |
| L MM | 0.50 | 0.70 |
| e1 MM | 0.65 BSC |
| B MM | 0.18 | 0.30 |
| D MM | 6.40 | 6.90 |
| E MM | 4.40 NOM |
| G MM | 0.25 REF |
| H MM | 6.25 | 6.55 |
| phi | 0° | 8° |